## Slide 1: Smart Charger Specification Updates
David Heacock Benchmarq; a Unitrode Company

## Slide 2: Charger Updates
Proposed specification v1.08
  No feature changes
  Remove unclear wording/descriptions
  Maintain compatibility with v1.0
  Clarified accuracy issues
  Clarified Host controlled charger
Please comment to proposed changes by 11/30/98

## Slide 3: Charger Updates Details
Thermistor renamed to safety signal
  Eliminates confusion
  Provides necessary safety component between Smart Battery and Charger
  Allows use of a resistor to indicate wake-up charge timeouts
Remove terms Host Controlled and Smart Battery Controlled
  Level 3 and Level 2 charge types
  Level 3 can poll the battery or in slave-mode, have its own termination algorithm

## Slide 4: Charger Updates Details (cont’d.)
Clarified regulation accuracy to a minimum of 5% for current and voltage
  Representative of what the charger is capable of providing
Current and voltage “not in regulation” bits were made optional
Added tolerance to Safety Signal Chart
Recommended charger leakage current of less than 100A