## Slide 1
“PCC” Preliminary Platform (System side)
Oct-22-1998
Yosuke Konaka / Hitachi, Ltd. PCD
konaka@ebina.hitachi.co.jp
HITACHI, Ltd.

## Slide 2
Back word compatibility
-System Side Detection Protocol
Step1)Check Battery Mode ( ) Bit10:PCC bit /No “PCC”.
Step2)If Find “1:PCC Support” ,Tentative Enable “PCC”.
Step3)Recheck Battery Mode ( ) /with “PCC”
Step4)If Fond “PCC” Error , go back to Step1
If not found “PCC” Error then enable “PCC” Cycle.
-Why need “Detection Protocol”
*Some Smbus Slave doing hangup with what begin to be read
more than byte number of rule in order to confirm PCC.
*Some Smbus Slave return wring data with begin to be read
more than byte number.
HITACHI, Ltd.

## Slide 3
HITACHI, Ltd.
”PCC Battery” can mix “non PCC System”
Pattern.1 Pattern.2 Pattern.3 Pattern.4
System w/o PCC w/o PCC PCC PCC
Battery w/o PCC PCC w/o PCC PCC
===============================================
n.p Case1 Case2 n.p
-Case1
STOP sequence is published than the system side by a byte
number of rule, and battery side can recognize do not need "PCC”
-Case2
System side can identify whether the battery side supports "PCC"
by battery detection sequence.