## Slide 1
“PCC” Preliminary Platform (System side)
Oct-22-1998
Hitachi, Ltd. PCD
HITACHI, Ltd.

## Slide 2
Back word compatibility
-System Side Detection Protocol
Step1)Check Battery Mode ( ) Bit10:PCC bit /No “PCC”.
Step2)If Find “1:PCC Support” ,Tentative Enable “PCC”.
Step3)Recheck Battery Mode ( ) /with “PCC”
Step4)If Fond “PCC” Error , go back to Step1
If not found “PCC” Error then enable “PCC” Cycle.
-Why need “Detection Protocol”
*Some Smbus Slave doing hangup with what begin to be read
more than byte number of rule in order to confirm PCC.
*Some Smbus Slave return wring data with begin to be read
more than byte number.
HITACHI, Ltd.

## Slide 3
HITACHI, Ltd.
”PCC Battery” can mix “non PCC System”
Pattern.1 Pattern.2 Pattern.3 Pattern.4
System w/o PCC w/o PCC PCC PCC
Battery w/o PCC PCC w/o PCC PCC
===============================================
n.p Case1 Case2 n.p
-Case1
STOP sequence is published than the system side by a byte
number of rule, and battery side can recognize do not need "PCC”
-Case2
System side can identify whether the battery side supports "PCC"
by battery detection sequence.

## Slide 4
ﾊﾞｯﾃﾘﾊﾟｯｸのSMBus通信中における抜差による誤書込
脱着による誤Ｗｒｉｔｅ．．．BatteryはHot plug in/outされる。
Smat BatteryのRead/Write 兼用Command
    Remaining Capacity Alarm (0x01)
    Remaining Time Alarm (0x02)
    Battery Mode (0x03)
    AtRate(0x04)
ReadとWriteとのProtocolの違い
Read CommandとWrite CommandとのProtocolの違いを上図に示すが、この違いは
2byte目のCommand Codeの後のRestartの有無、及び総バイト数だけ（Read:5byte,
Write:4byte）であり、Restart bitが欠落した場合ReadをWriteと判断し誤書き込みを
するおそれがある。
以下に誤書込について、簡易検証した結果を例として示す。
HITACHI, Ltd.

## Slide 5
HITACHI, Ltd.
ﾃﾞｰﾀの信頼性向上
充電時の基礎方式を決定する,ChargeVolatege( ),ChargeCurrent( ),Chemistry等を誤ってﾁｬｰｼﾞｬが 取得した場合、何度も読み出しｺﾝﾍﾟｱする程度しか、ｴﾗｰ検出手段がない。
２個のバッテリを充電するシステムにおいて、充電停止条件としてTerminate Charge Alarm Flag を
使用しているばあい、突然他方のバッテリに充電が移る可能性がある。
BatteryStatusも同様。 放電中にFully Discharge Alarmを誤読出し、突然ｻｽﾍﾟﾝﾄﾞに遷移する可能性
もある。
逆に、充電中は、充電が突然停止する可能性もある。