## Slide 1: SMBus Version 1.1
John Milios USAR Systems

## Slide 2: Agenda
SMBus - besides batteries
New in Version 1.1
  Electrical specification
  Protocols
  Stand-alone specifications
Building reliable SMBus systems
What is next

## Slide 3: SMBus - Besides batteries
SMBus is adopted as the system control bus beyond the Smart Battery System
New platforms
  Notebook
  Desktop
  Server

## Slide 4: SMBus in Notebooks
Smart Battery System
Docking
Notebook thermal zones
Fan speed control
Power planes control

## Slide 5: SMBus in desktops
Thermal zones
Fan speed
Memory Serial Presence Detect
Communications control assistance

## Slide 6: SMBus in Servers
Intelligent Platform Management Initiative
Baseboard controller
Chassis controller
Diagnostics & monitoring

## Slide 7: System interface
Several SMBus branches can interface to the system
  Through the Embedded Controller
  Through the chip-set

## Slide 8: Chipset interface
Intel 82371EB SMBus is an ISA device
  Static resources
  BIOS sets I/O range
  IRQ fixed at IRQ 9
Access to individual devices
  Through ACPI driver
  or through OEM drivers

## Slide 9: SMBus through the Embedded Controller
EC register interface (ACPI specs)
SMBus host interface (ACPI specs)
Multiple SMBus branches can be addressed via the SB selector or transparently through the EC
Devices are accessed with hard-wired addresses
  Through SMBus/Device class drivers
  Through ACPI control methods

## Slide 10: New in Version 1.1
Relaxed electrical specification
Packet Error Checking
Stand-alone specifications

## Slide 11: Electrical specifications
Operation between 3 and 5 Volts
Logic levels of SMBus devices conform to 3 Volt CMOS levels
Compatible with devices operating at 2 Volts

## Slide 12: SMBus model
SCL
SDA
RP
VDD = 5 V
VIH0,MIN = 3.5V
VIL0,MAX = 1.5V
VIH1,MIN = 2.1V
VIL1,MAX = 0.9V
VIH2,MIN = 1.4V
VIL2,MAX = 0.6V
VDD1 = 3 V
VDD2 = 2 V

## Slide 13: Logic levels
SMBus DC Low State
VIL2,MAX
0.6
0.4
0.8
0.9
1.5
1.4
2.1
3.5
VIL1,MAX
VIL0,MAX
VIH2,MIN
VIH1,MIN
VIH0,MIN
VOL,MAX
VIL,MAX
VIH,MIN
1
2
Device 2 starts counting THIGH
Device 1 starts counting THIGH
5.5
VIH,MAX
SMBus DC High State
3
Device 0 starts counting THIGH
0.65
2.25
SMBus
Rise Time
Definition

## Slide 14: Reliability & error recovery
Error detection mechanisms
  Packet Error Checking (PEC) introduced in version 1.1 of the specifications
Address
Data 1
Data N
...
Packet Check Byte
Address
Data 1
Data N
...

## Slide 15
Interoperability & PEC auto-detection
A PEC Master checks and registers the capability of the Slave it is addressing
A PEC Slave always responds with LRC in a Master initiated Read type of protocol
S
Slave Address
R
A
Data Byte
NA
PEC
S
Slave Address
R
A
Data Byte
A
Receive Byte
P
NA
P
Packet Check Byte is implemented over the whole
transaction including address and R/W fields

## Slide 16: Stand-alone specification

## Slide 17: Reliable SMBus systems
SCL
SDA
SMBus
Device
Rp
VDD
Hi
Lo
Hi
Lo
or
or
Low cost
Exponential signal rise
Higher cost
Linear rise
Tolerates large bus capacitance
Hi current source during signal rise
Low current source when signal is low
ICs from Linear Technologies

## Slide 18
Design constraints
IPULLUP,MAX* = 350 uA
    Determined primarily by the series protection resistors in Smart Batteries
    Devices should be able to maintain VOL,MAX while sinking 350uA
Maximum Rise Time: 1000 ns
    Determined by need to achieve maximum bit transfer rate of 100Kbs, as 20% of clock high half period (4 us min)
    Affects the maximum bus capacity if you use Pull-ups or simple current souces
Constraints apply to each individual SMBus branch *Actual pull-up current can be larger if the sink current does not exceed 350 uA

## Slide 19: What is next
Dynamic addressing
Inclusion of SMBus in PCI connector specifications

## Slide 20: More information
Download the SMBus specifications from: www.sbs-forum.org
Give feedback to feedback@sbs-forum.org
Ask questions to: jmilios@usar.com