## Slide 1: Smart Battery Data Accuracy Specification
Phil Mummah
October 1998

## Slide 2: Purpose
Give confidence that charger will fully charge battery based on data, not voltage reading
Give confidence to user that time remaining is accurate
Show importance of “re-calibration” capability for notebooks
Certify batteries with a pass/no pass evaluation

## Slide 3: Test Basics
Test the accuracy of the data reported by smart batteries
Test equipment compares charge energy and discharge energy with battery reported data
Six basic tests with multiple parts
  Test emulate real notebook environment
    After full discharge and full charge
    After partial discharging and partial charging
    After prolonged storage

## Slide 4: Specification Feedback
Current revision number 0.8
Smart Battery Data Accuracy Specification is on the web
  http://www.sbs-forum.org
Review and give feedback to:
  feedback@sbs-forum.org

## Slide 5: Test Setup Example
Reads Voltage/Current
Measure voltage/current
Output control to charger
Programmable
Charger
&
Load
SMBus
Voltage
Current
Monitor
Battery
Output
commands
to charger

## Slide 6: Test Descriptions
Test defines
  Full charge
  Full discharge
  Loads
  Calibrate battery
  Test temperature
  Parameters to measure/read
    Measure -> Read using external equipment
    Read -> Read over SMBus
Tests start with calibrated battery
  Known starting point
Record and plot:
  Measured verses read parameters

## Slide 7: Test 1
Calibrate battery
Full charge and full discharge battery five times
Charge battery at full requested rate
Tests battery under optimal conditions

## Slide 8: Test 2
Calibrate battery
Full charge and partial discharge battery to 35% capacity five times
Current limit charging current to C/2
Repeat test with variable load

## Slide 9: Test 3
Calibrate battery
Partial charge to 80% and partial discharge battery to 30% capacity five times
Charge battery at full requested rate
Repeat test with variable load

## Slide 10: Test 4
Discharge battery at 1C rate
Step change discharge rate to
  1/2 C
  70 MA
  12 MA
  70 MA
  1/2 C
  1 C
Plot recorded and reported values

## Slide 11: Test 5
Calibrate battery
Store battery 48 hours between 20 & 25 degrees C
Discharge battery and record:
  Max error
  Energy removed from battery
Repeat at 40 degrees
Repeat, storing 7 days between 20 & 25 degrees C

## Slide 12: Test 6
Record cycle count
Over discharge battery
Connect to 12 volts
Verify SMBus communication restored
Verify cycle count restored