## Slide 1: SMBus Architecture Overview & Integration With OS Phil Mummah Intel® Corporation
Copyright © 1998 SBS Implementers Forum, All Rights Reserved
®

## Slide 2: Agenda
SMBus in a mobile system
Access in Windows* NT 5.0
Access in Windows* 98
82371EB (PIIX-4E) SMBus
* Other trademarks and brands are the property of their respective owners
All products, plans and dates are preliminary and subject to change without any notice.
®
Notes: Today I will talk about:
1. SMBus(es) in a mobile system
2. Accessing SMBus devices in an NT environment
3. Accessing SMBus devices in a Win 98 environment
4. Finally, I will talk about the SMB architecture in a PIIX-4E environment,
including a legacy environment.

## Slide 3: SMBus in Mobile Systems
Many mobile systems implement SMBus interface and devices
  Smart battery subsystem
  Thermal sensor
  Memory modules
    SPD (serial presence detect) for sizing
More than one SMBus may exist in a system
  ACPI defined SMBus behind an embedded controller (EC)
    Defined in chapter 13 of ACPI specification
  82371EB (PIIX-4E) SMBus
Applications need to retrieve information from these devices
  Different drivers necessary for each SMBus type
®
Notes: SMBus is becoming very popular with new designs. The number of components that support SMBus is growing. Some systems even have more than one SMBus. One may be used for a battery system
and another may be used for other devices such as back light control or memory serial presence
detect. This has brought about a requirement to access these new devices via software.
The s/w solution is distinct for each SMBus type, the OEM requirements and the OS environment.
ACPI defines an SMBus interface, with an SMBus behind an embedded controller that has a
standard interface. This does not mean that other SMBus architectures are not ACPI compliant. It
just means that if the OS is to directly access the SMBus it must conform to the defined interface.

## Slide 4: Smart Battery Architectures
Charger
Host Controller/Embedded Controller
Battery
Battery
Selector
S/W or Driver Stack
S/W
H/W
SMBus
Commands
Recommended
SMBus Commands
Optional Voltage
Monitoring
Smart Battery
Compatible to User
OS Compatibility Entry Point
Control Method or Smart Battery?
SMBus
Other SMB Devices

## Slide 5: SMBus Access in Windows* NT 5.0
In Windows* NT 5.0 ACPI tables define an SMBus host controller
  Device object with _HID value “ACPI0001”
Windows* NT 5.0 will load SMBus driver and own the bus resources if an ACPI compliant EC with Smart Battery System is detected
  System apps regularly request information from the SMBus driver
* Other trademarks and brands are the property of their respective owners
®
Notes: In Win NT 5.0, at boot up, the OS will check the ACPI tables to see if an ACPI defined SMBus
behind an embedded controller exists. If it does, and there is a smart battery system present, it will
load the smart battery driver. Since it is a standard I/F, the OS can directly access the SMBus and
determine if a smart battery system exists. The OS owns the resources (I/O port) to the EC.
System applets can then request battery information through this driver. They can not directly
access the embedded controller since the OS owns the EC resources.

## Slide 6: SMBus Access in Windows* NT 5.0
OEM Driver may access SMBus devices through
  SMBus Host Controller Driver: Recommended
    Generic, works on all systems running Windows* NT 5.0
  Control Methods
    Function calls from driver must be implemented by control methods in ROM
    If function calls are not standard, driver will not work on all systems
  Smart Battery Driver
    Supports battery commands only
      OS uses sub-set of smart battery commands in its applet
    Not viable to access non-SBS devices
* Other trademarks and brands are the property of their respective owners
®
Notes: There are three ways an OEM driver/applet can access SMBus devices.
This includes battery devices as well as other devices.
1. The recommended method is through the SM Bus host controller. This
is a generic method that works on all systems running NT 5.0. All types
of devices can be access using this method.
Advantages: works on all NT 5.0 systems and for all SMBus devices.
2. Control methods: All SMBus devices and all of their functions can be
accessed this way, however, all functions must be supported in the ACPI
ROM. This is a very good way to access devices on one particular platform.
An OEM can use this to add custom functionality to his platform.
Advantages: Works for all devices.
Disadvantages: Support routines must be built into the system ROM
This means it is probably platform specific.
3. Smart battery driver: This is a good way to access
battery devices but not other type of devices.

## Slide 7: NT 5.0 SMBus Access
OEM Driver
SMBus Host Controller Driver
Embedded Controller Driver
System OS Apps
Smart Battery Driver
ACPI Defined SMBus
Smart
Battery
System
OEM
Device
OEM Device with
SMB Request (IRP)
OEM App
Embedded Controller
Battery Commands
Thermal
Device
ACPI Driver
S/W
H/W
Driver commands
must be supported
by control methods
in the system ROM
* Other trademarks and brands are the property of their respective owners
®
Notes: This is a functional diagram of the battery driver stack. The drivers inside
the dotted lines are loaded if NT detects a smart battery system behind
an ACPI defined SMBus.
This shows the three methods of accessing SMBus devices.
1. Through the SMBus host controller driver
2. Through ACPI driver, ie, through control methods.
3. Through the smart battery driver.

## Slide 8: SMBus Driver Interface
SMBus driver defines interfaces available through the DeviceIoControl function to other kernel-mode drivers
  SMB_BUS_REQUEST
    Handles all SMBus transactions
  SMB_REGISTER_ALARM_NOTIFY
    Allows user to register a callback function for SMBus alarm notification
  SMB_DEREGISTER_ALARM_NOTIFY
    Un-register callback function for SMBus alarm notification
®
Notes: The recommended method of accessing OEM SMBus devices is using the SMBus host
controller I/F. This is described in Microsoft’s DDK.
There are three basic commands:
SMBus request, register alarm, deregister alarm.

## Slide 9: SMBus Access in Windows* 98
Smart Battery Driver and SMBus Host Controller Driver are not loaded in Windows* 98
Program interface to SMBus is through control methods or through the Embedded Controller Driver
  Battery control methods defined in ACPI specification
    Sub-set of smart battery commands
    OS only uses these commands to access battery sub-system
  OEM can define super-set of battery commands and implement in control methods
    Applet/Driver can then call control methods
    Applet/Driver will only work on system that has the extra commands in ROM
  Generic access to SMBus would be through the Embedded Controller (EC) Driver
    EC driver arbitrates access to the embedded controller
* Other trademarks and brands are the property of their respective owners
®
Notes: SMBus access in Windows 98 is different than in NT 5.0. Most importantly
the SMBus host controller driver are not loaded in Win 98! This removes the
recommended interface to the SMBus. Two methods are available:
1. Through control methods. All commands for a device can be supported
however the commands must be supported by the ACPI ROM. This means
accessing devices in this manner will be platform specific. This is a good
method to customize an OEM’s platform.
2. Generic access to the SMBus is through the embedded controller driver.
Direct access to the EC is not allowed as the EC driver needs to arbitrate
multiple threads that may be accessing the controller simultaneously.

## Slide 10: Windows* 98 SMBus Access
Driver
Embedded Controller Driver
ACPI Defined SMBus
(Smart)
Battery
System
OEM
Device
(Thermal
Sensor)
OEM App
Embedded Controller
OS App
ACPI Driver
S/W
H/W
* Other trademarks and brands are the property of their respective owners
®
Notes: Here you see the Win 98 driver stack. The dotted line again divides h/w
and s/w. As you can see the smart battery driver and the SMBus host
controller driver are not loaded.
This also shows the two methods of accessing SMBus devices, through
the ACPI driver, ie control methods, or through the embedded controller
driver.

## Slide 11: 82371EB (PIIX-4E) SMBus
Not ACPI defined SMBus
  ACPI defined SMBus is behind an embedded controller
  Defined in ACPI spec, chapter 13
82371EB SMBus is NOT a PCI device
  Does not show up in PCI config space (Offset 00-040H)
82371EB SMBus is an ISA device
  Static resources
  BIOS sets I/O range
  IRQ fixed at IRQ 9
Do not put battery systems (charger) on this bus
  Use for thermal devices, RAM SPD, Back light control
®
Notes: Let speak briefly about ACPI and SMBus. ACPI defines a specific SMBus I/F. It resides behind
an embedded controller and has a defined mechanism to access devices on the SMBus. When the OS sees this type of SMBus it knows how to directly query devices on it without using control methods.
I do not want to imply that other types of SMBuses are not ACPI compliant! The PIIX-4E
SMBus is ACPI compliant. It does not have the same I/F that is defined in chapter 13 and it is not
a PCI device. It is an ISA device with static resources. This can be described in the ACPI tables
and control methods can be defined to access it.

## Slide 12: 82371EB (PIIX-4E) SMBus
Chipset/SMBus Host Controller
82371EB SMBus
Thermal
Sensor
OEM
Device
OEM App
ACPI Driver
OS Thermal App
S/W
H/W
If thermal sensor on
82371EB SMBus (OS owns resources)
If OS does not
own resources
OR
Possible
Standard
Driver
OEM
Driver
OR
®
Notes: Here is a diagram of the PIIX-4E SMBus controller. As you can see there
are three ways shown here to access it, however, only one can be used.
The issues is that if multiple threads/drivers access it with nothing doing the
arbitration, then commands can get lost or sent incorrectly. This is because
the I/F to the controller is first a command and then a data byte. If a second
thread sends a command after a previous thread had send a command, then
the second command byte will be interpreted as a data byte and the first
thread data will be a command byte.
If the thermal sensor is on this bus then the ACPI driver owns the I/F to the
SMBus.
Solutions:
1. Put all device commands in control methods. This is good for a platform
solution, but it is not a generic solution.
2. Define a standard set of ACPI commands for specific devices. There
are groups doing this. This would allow a standard driver to be loaded
and general applets would then access this driver.
3. The third solution would be to put only OEM specific devices on the
bus and write control methods to access them.
For questions or feedback, please use this web site:
Feedback@sbs-forum.org

## Slide 13: Back Up

## Slide 14: Request SMBus Transaction
OEM driver makes SMBus transaction request to the SMB driver
  Initiate an IRP_MJ_INTERNAL_DEVICE_CONTROL IRP with the IOCTL code of SMB_BUS_REQUEST
    Pass SMBus protocol, device address as input parameters.
  SMB driver returns data to the OEM driver

## Slide 15: Request SMBus Transaction
Read a word from SMB device
SMB_REQUEST SmbReq;
SmbReq.Protocol = SMB_READ_WORD;
SmbReq.Address = DeviceSmbAddress;
SmbReq.Command = SmbCmd;
. . .
// Build a IRP to send to the SMB driver
Irp = IoAllocateIrp(SmbHcFdo->StackSize, FALSE); // alocate memory
IrpSp = IoGetNextIrpStackLocation(Irp); // point to stack location
IrpSp->MajorFunction = IRP_MJ_INTERNAL_DEVICE_CONTROL;
IrpSp->Parameters.DeviceIoControl.IoControlCode = SMB_BUS_REQUEST;
IrpSp->Parameters.DeviceIoControl.InputBufferLength = sizeof(SMB_REQUEST);
IrpSp->Parameters.DeviceIoControl.Type3InputBuffer = SmbReq;
IoSetCompletionRoutine(Irp, OEMDevSyncRequest, &Event, …);

## Slide 16: Request SMBus Transaction
Read a word from SMBus device (Con’t)
// Send IRP to SMB driver
IoCallDriver(SmbHcFdo, Irp);
KeWaitForSingleObject(&Event, Executive, KernelMode, FALSE, NULL);
Status = Irp->IoStatus.Status;
IoFreeIrp(Irp);
. . .
// Fetch Data
If(NT_SUCCESS(Status))
*DataWord = SmbReq.Data[0] | (SmbReq.Data[1] << 8);

## Slide 17: Register For SMBus Alarm
OEM driver initiates an IRP_MJ_INTERNAL_DEVICE_CONTROL IRP with the IOCTL code of SMB_REGISTER_ALARM_NOTIFY
  Pass device addresses to generate alarm as input parameters
  Pass callback function as input parameter

## Slide 18: Register for SMBus Alarm
Register callback functions for SMBus alarm
SMB_REGISTER_ALARM registerAlarm;
registerAlarm.MinAddress = DeviceSmbMinAddress;
registerAlarm.MaxAddress = DeviceSmbMaxAddress;
registerAlarm.NotifyFunction = NotifyFunction;
registerAlarm.NotifyContext = NotifyContext;
. . .
// Build a IRP to send to the SMB driver
Irp = IoAllocateIrp(SmbHcFdo->StackSize, FALSE); // alocate memory
IrpSp = IoGetNextIrpStackLocation(Irp); // point to stack location
IrpSp->MajorFunction = IRP_MJ_INTERNAL_DEVICE_CONTROL;
IrpSp->Parameters.DeviceIoControl.IoControlCode = SMB_REGISTER_ALARM;
IrpSp->Parameters.DeviceIoControl.InputBufferLength = sizeof(SMB_REGISTER_ALARM);
IrpSp->Parameters.DeviceIoControl.Type3InputBuffer = registerAlarm;

## Slide 19: Register for SMBus Alarm
Register callback function (Con’t)
// Send IRP to SMB driver
IoCallDriver(SmbHcFdo, Irp);
KeWaitForSingleObject(&Event, Executive, KernelMode, FALSE, NULL);
Status = Irp->IoStatus.Status;
IoFreeIrp(Irp);
. . .
// OEM driver’s callback function
NotifyFunction(){
. . .
}

## Slide 20: ACPI Hardware and Software Tools and Demo

## Slide 21: Windows* 98 with Smart Batteries
Equipment
  Fujitsu* notebook running Windows 98
  Pentium® Processor with MMX
SBS-Forum driver
OS battery applet interfaces to batteries with no firmware
* Other trademarks and brands are the property of their respective owners

## Slide 22: Windows* 98 with Smart Batteries
Equipment
  Trajan reference platform running Windows 98
  Pentium® II Processor with MMX
OEM style applet
  Interfaces to battery system
  Tests all smart battery commands
All SMBus commands (non-battery) possible
  Allows programmable access to other devices